## Slide 1: Water Wise Gardening
February 8, 2020
Manotick Horticultural Society
Rebecca Last – Master Gardeners of Ottawa-Carleton
Photo by Aaron Burden
Notes: I had a lot of help building this presentations.
Fellow Master Gardeners generously shared their photos and wisdom.
So throughout this presentation, you will see me giving credit to the many talented gardeners who lent me their photos and knowledge.
Also, this presentation is intended as an introduction to an extensive topic.
Most of the sections of this presentation could be expanded to make a presentation all on their own.
Consequently, we will be covering a lot of ground, and I won’t be going into much detail.
Fortunately, there are tons of resources and DIY information on line should you wish to explore any of these topics in more detail.

## Slide 2: Outline
Why conserve water?
Preventing run-off
Harvesting water
Best practices for watering
Conserving soil moisture
Plant selection
Putting it all together
Conclusions
Q&A

## Slide 3: Why conserve water?
Save money on water bills
Deal with climate change
Manage extreme weather (droughts and floods)
Preserve ground water

## Slide 4: 2. Saving Money by Saving Water
Notes: Water bill from my house July 2020
Tiered water pricing is a bit like graduated income tax.
The marginal price of water increases as you use more.
The price jump from tier one (0-6 cubic meters of water used per month) to Tier 2 (7-25 cubic meters per month) is almost double.
Like many municipalities, Ottawa is also paying down new water infrastructure, so there is an additional cost for wastewater treatment.
So saving money is an important reason for saving water

## Slide 5: 2. Climate Change & Extreme Weather
Notes: The unfolding story of climate change impacts is that there will be regional variances in precipitation.
NE North America, where we live, is likely to see more precipitation.
But in general, water will become less available. Faster spring melts and shrinking glaciers are likely to move water from land to the sea.
The story is one of extremes – more flood events, but also more droughts.
How serious might water shortages get?
Water began trading on the Wall Street alongside oil and gold for the first time in early December, 2020!!

## Slide 6: Preventing run-off
Redirect down-spouts
Rain gardens
Green roofs
Swales
Notes: So our first step in water-wise gardening is to try to prevent water just running off our property
We want to slow down the flow of water and give it a chance to soak into the soil.
This way, we can make the most of rainfall when it happens,
And help to re-charge ground water in our area.
There are lots of other benefits to slowing rain water run-off:
  We see less soil erosion
  Less sediment and pollutants wind up in our streams and waterways
  And municipalities don’t have to spend as much money ensuring we have clean drinking water.

## Slide 7: 3a. Redirect down-spouts
Photos courtesy of Joan Nieman-Agapas, SCMG
Notes: The down-spouts in these photos are draining directly onto hard surfaces.
They’re also really close to the foundations of the house, so that’s not good either.
Rain coming out of these down-spouts will immediately run off into the nearest storm sewer.
It doesn’t have any chance to infiltrate the soil.
It’s not going to do the garden any good at all.
And it’s not recharging groundwater.

## Slide 8: 3a. Redirect down-spouts
Photos courtesy of Joan Nieman-Agapas, SCMG
Notes: These down-spouts have been redirected away from the foundations of the home, which is good.
They direct the water onto permeable surfaces – grass, a flower bed.
This means that rain water will have a chance to infiltrate the ground and re-charge ground-water.
It also means we’re taking advantage of the rain to water the grass and flowers.
That’s water we don’t have to take from the tap and we don’t have to pay for it.

## Slide 9: 3b. Rain gardens – Homeowner
Notes: This photo is from the Buncombe County Master Gardeners in North Carolina.
Note that cascade of gravel is on the down-slope. Its purpose is to stabilize the soil while facilitating run off of surplus water.
Steps to build:
  Call utilities first – you’re going to be digging and you don’t what to hit any underground utilities
  Know your soil type – sand, loam or clay will all drain at different rates
  Do a drainage test – dig a hole, insert a measuring stick, fill with water and see how fast it drains
Speed of drainage will determine both how much you amend the soil and what you plant.
Slow draining soil will require you to add more SHARP sand and compost, and plant with more wet-loving plants. Note, if you have clay soil, do not add just any old sand because the result may be something like concrete. Use builders or sharp sand to increase drainage.
For quick-draining locations, add more organic material to your back-fill and pick drought-tolerant plants.
Either way, your rain garden should be designed to drain within 48 hours.
The size of your rain garden should be based at least partly on the area of roof that is draining into it. Typically a rain garden is at least 5% to 10% of the area of the roof draining into it.
Don’t forget that your rain garden is essentially a basin, so if you don’t have enough square footage to go horizontal, go vertical. Dig your rain garden a little deeper.

## Slide 10: 3b. Rain gardens – Homeowner
Image courtesy of Toronto and Region Conservation Authority. See: https://trca.ca/news/complete-guide-building-maintaining-rain-garden/
Notes: Profile view of rain garden
Situate your rain garden when it can easily collect run-off. For example, near a down-spout
Dig down at least 85 cm. Go deeper if your rain garden is going to be smaller than 5% of the roof area.
Line the bottom of the hole with material that drains easily – sharp sand, builders’ sand or fine gravel.
On top of that, pile in the garden soil, amended with compost to make a rich, organic mix.
The top this with a layer of shredded wood mulch.
Edge your rain garden with rocks to stabilize the soil and provide definition that will enhance the appearance.
On the up-slope, use rocks as a kind of “speed bump” to slow incoming water.
On the down-slope pile extra soil to create a kind of berm to retain water, and use edging rocks to further stabilize soil in case of water run off.
Plant your rain garden with species that don’t mind being inundated with water, and are also drought tolerant. Native plants are your best bet.
If your soil drains slowly, you can even use water garden plants in the middle of your rain garden, whereas the more drought-tolerant species should be positioned closer to the edge of the garden.
Also, make sure that plants in the centre of your rain garden are tall enough to poke out of the water when the garden is full of water.
This idea of having taller plants in the middle of an island bed is also just good garden design because it means that the taller plants are visible from all angles

## Slide 11: 3a. Rain gardens – Municipal
Photo courtesy of Sean James
Notes: Rain gardens are increasingly part of municipal water management strategies.
This photo is from Mississauga and the design includes porous pavers for the parking area
Water is able to infiltrate through the surface of the parking lot.
The diagram on the sign illustrates how that infiltrated water is channeled into the rain garden beds.

## Slide 12: 3c. Green roofs
Notes: Another way to prevent run-off is to build green rooves where plant material can soak up the water that hits the otherwise hard surface of our roof.
Retro-fitting a home for a green roof is a complex and costly business.
Most green roofs are purpose built, often on public buildings.
The green roof on the building trades building at Algonquin College is a great example because it serves as a demonstration for students.

## Slide 13: 3c. Green roofs
The initial structure. Photo courtesy of Tena van Andel, Toronto Master Gardeners.
Notes: But some home-owners are able to go the extra mile, like Master Gardener Tena Van Andel who built a green roof on a pergola in her back yard.

## Slide 14: 3c. Green roofs
Water proof membrane lines the roof. Photo courtesy of Tena van Andel, Toronto Master Gardeners.
Notes: This requires both space and a high level of expertise.
In other words, don’t try this at home without a lot of research and / or professional assistance.

## Slide 15: 3c. Green roofs
Gorgeous results with sedum in bloom. Photo courtesy of Tena van Andel, Toronto Master Gardeners.
Notes: Note the drought resistant plants selected for this location. Sedums and Russian sage will withstand downpours and the hot dry conditions on a roof-top.
Tena says that, when the sedums are in bloom, this is her favorite garden view.

## Slide 16: 3d. Swales
Notes: We wrap up this section on preventing run-off with a technique that actually merges into the section on capturing rain water.
A swale is essentially a ditch dug parallel to and near the bottom of a slope.
This ditch is designed to collect rain water, slow its run off and give the water time to soak into the ground.
According to the Natural Water Retention Measures site of the EU:
  Swales are broad, shallow, linear vegetated channels which can store or convey surface water (reducing runoff rates and volumes) and remove pollutants. They can be used as conveyance features to pass the runoff to the next stage of the SuDS treatment train and can be designed to promote infiltration where soil and groundwater conditions allow. Three kinds of swale give different surface water management capabilities:
    Standard conveyance swale – Generally used to convey runoff from the drainage catchment to another stage of a SuDS train. They may be lined or un-lined, depending on the suitability for infiltration.
    Enhanced dry swale – Includes an underdrain filter bed of soil beneath the vegetated conveyance channel to accommodate extra treatment and conveyance capacity above that of the standard swale. The underdrain leaves the main channel dry except for larger runoff events, and will prevent channels becoming waterlogged where the swale is situated on gentler slopes. A lining can also be incorporated into the underdrain if infiltration to underlying ground is not appropriate.
    Wet swale - Where prolonged treatment processes are required for the storm runoff, the swale’s conveyance channel can be encouraged to maintain marshy conditions by using liners to control infiltration, or by siting in an area with high water table.
The top picture looks more like a wet swale, designed to hold run off at the surface for a day or two.
The lower photo looks more like a standard conveyance swale.
Again, these structures are often used in municipal water management strategies.

## Slide 17: 3d. Swales
Notes: However, homeowners with larger gardens or sloped gardens may also implement swales.
Here are a couple of examples of dry stone creeks that serve as swales during wet weather.
Having done something similar in my front yard, my big take-away is that I should have spent more time grading the channel to make it more effective in capturing rain water.

## Slide 18: 3d. Swales
Photo courtesy of Susan Bicket, Master Gardeners of Ottawa-Carleton
Notes: This swale is on the property of a fellow Master Gardener from the Ottawa area.
Susan has a large property and clay soil.
She also gardens on well-water, so every drop is precious – even the surplus spring run-off!
In fact, there are kind of two swales at right angles to each other here.
In the centre of the photo that rocky path drains water from the outlet for the house’s sump pump into the swale.
You can see how lush and green the swale is, even in the midst of a drought that has browned a lot of the turf grass.

## Slide 19: Harvesting water
Rain barrels
Grey water usage
Notes: Now we turn to ways in which we can harvest water
The obvious thought here is to harvest rain-water, which is great
But don’t forget about ways you can re-use waste water from your home.

## Slide 20: 4a. Rain barrels
Notes: If you have a roof, you should have at least one rain barrel.
Your first step to installing rain barrels is to ensure that you have gutters and down-spouts around your roof.
With a mansard roof like the one on my house, the near vertical roof surface can be challenging. We regularly have to maintain our roof gutters.
Another thing I discovered when I started using rain barrels is that they don’t work with soaker hoses.
Soaker hoses require 30 pounds / square inch of water pressure
Each foot of elevation creates 1 pound / square inch of water pressure.
So to use soaker hoses with my rain barrels, I’d need to put the rain barrels on the roof of the house. Even then, I might not get enough pressure!

## Slide 21: 4a. Rain barrels
What to look for in a rain barrel
Durable materials
Stable when full
Child proof / animal proof
Top screen
Overflow valve
Durable, leak-free spigot
Manufacturer’s guarantee
Photo courtesy of Gayle Quick, MGOC
Notes: So what to look for in a good rain barrel?
  Choose a barrel made of durable materials.. Clay barrels looks very classy but are unlikely to last more than one season!
  Is it safe for children and wildlife? Make sure the barrel has a stable design that won’t tip over.
  Some barrels come with a flat back so they can be secured to a wall or fence.
  A screen on top of the barrel will prevent debris and wildlife from falling in, and mosquitos from laying their eggs.
  Ensure at least one over-flow outlet, two are better. This regulates the flow of water in the barrel
  Can you link two or more barrels together as shown in this illustration? Look for this feature so you can develop better water harvesting in the future.
  Ensure it has a durable spigot and leak-free housing for the spigot.
  And try to get a barrel that has a manufacturer’s guarantee against faulty parts or manufacturing flaws.
By the way, the containers shown in the foreground of this photo are self-watering – another strategy to minimize both your labour and the amount of watering they require.

## Slide 22: 4a. Rain barrels
If you have the space, this 1,000 liter “water tote” is cheaper alternative to stringing several barrels together.
The owner is planning to grow vines up the sides to camouflage it.
Photo courtesy of Catherine Disley, MGOC

## Slide 23: 4b. Grey water usage
Notes: Grey water is the waste water from washing yourself, dishes, veggies, etc. It is different from “black water”, which is another term for sewage.
One of my earliest memories of grey water harvesting comes from a visit to this farm in South Australia.
This photo would have been taken about 1963.
That’s me in the red skirt with our family friend Alan Fry.
We stayed over with the Frys on our long drive from Sydney to Adelaide to spend Christmas with my cousins.
It was early summer in Australia, but you can see how dry everything was!
We were allowed 2” of bath water and the water from the bath drained directly through the bathroom wall onto Mrs. Fry’s vegetable garden.

## Slide 24: 4b. Grey water usage
Notes: On a more modest scale, I capture water from my furnace in the winter.
On an average day, the furnace will produce 2-3 liters of condensate that drains into a utility sink in our laundry room.
Just outside the laundry room, is my little indoor grow-op, so I can use the furnace water to irrigate my plant starts.
The condensate is almost clear of any impurities – basically it’s distilled water – so it’s ideal for my delicate little seedlings.
In the summer, we run a dehumidifier in the basement.
During more humid months, it will produce up to 8 liters of quite clean water every day.
I will often take the full humidifier tank upstairs and out the side door where I can empty it only a side raised bed that is partially under the eaves of the house.

## Slide 25: 4b. Grey water usage
Other ways to collect grey water
Use a basin to collect water from the kitchen sink…
  When running water to get hot
  Doing dishes
  Cleaning vegetables and fruits
Harvest rinse water from the washing machine rinse cycle
Bring a bucket into the shower to collect that water, also
Notes: The Garden Myths website (https://www.gardenmyths.com/gray-water-safe-garden/#:~:text=Chemicals%20in%20Gray%20Water&text=The%20ones%20of%20concern%20with,use%20soap%20and%20not%20detergents.) has some useful notes on grey water usage.
The first thing he notes is that some jurisdictions have legal restrictions against using grey water. This does not appear to be the case for Ottawa, but check with your municipality.
There are three main concerns about using gray water in the garden:
  Chemicals
  Bacteria and
  pH
Grey water may contain chemicals such as sodium, boron and bleach, which can be harmful to plants. Sodium and boron are common ingredients in soaps and detergents. Even low concentrations of these chemicals can be toxic to plants.
Grey water may also contain bacteria, including human or animal fecal matter. If you suspect your grey water contains harmful bacteria, avoid using it on edible plants.
Finally the chemicals in soaps and detergents include various salts that can make your soil too alkaline.
Soils watered regularly with grey water can show elevated levels of boron and surfactants (the ingredient in soap that makes it foam or bubble.) Surfactants can also be harmful to amphibians – frogs, toads, salamanders, etc.
Chemicals in grey water can be especially harmful to plant leaves, so make sure to apply it directly to the soil.

## Slide 26: 4b. Grey water usage
Use your water resources wisely.
This Monstera plant has found a new happy place, growing inside a fish-tank
Photo courtesy of Caroline Novacek, Niagara Master Gardeners

## Slide 27: 5. Best practices for watering
Timing & Amounts
Tips for containers
Precision watering
  Watering spikes
  Ollas
  Drip irrigation

## Slide 28: 5a. Timing & Amounts
Photo by Alistair MacRobert
Notes: This is a very appealing image.
It speaks to summer, sun, kids playing in the sprinkler.
But it’s also a great illustration of all the WRONG things to do when watering.
Judging from the shadows, this photo was taken at midday, which is the worst time to water. On hot days, many plants will go dormant during the middle of the day, so they won’t be using any water you apply at midday.
That lovely rainbow in the image also illustrates the problems with this kind of watering. We’re spraying water into the air in the heat of the day. A good portion of that water will evaporate before it hits the ground.
Plus, there is no precision to this watering – we are delivering water over a wide area. That may be OK for turf grass, but in a vegetable or flower bed, we can save water by being more selective and delivering water exactly where it is most useful near the roots of the plants.
Finally, spraying water everywhere means that a lot of it winds up on the plants’ leaves. Leaves don’t absorb moisture; roots do. plus watering leaves can result in plants becoming more susceptible to fungal diseases like powdery mildew and blight.
So don’t water like this.

## Slide 29: 5a. Timing & Amounts
When to water
NOT midday
Early in the morning
Or in the evenings on very hot days
Overnight, to take advantage of cheaper rates.
How Much to water
Apply more water, less frequently
“tuna can” your lawn
Notes: When is the best time to water?
There is an old gardening joke that goes:
  When is the best time to water?
  When you think of it and have time!
As we have already discussed, watering at midday is a bad idea for all sorts of reasons.
Watering in the early morning is recommended because plants then get the water they need to do a full day of photosynthesizing. It’s like starting the day with a good breakfast.
On very hot days, watering in the evening may work even better as water has the chance to soak into the soil, ready for plants to use the next day.
Depending on where you live, utility rates may be lower over night. Remember, watering uses both power and water so you might save a few pennies by waiting for off-peak times.
How much should you water?
Daily sprinklings will encourage your plants to form more roots near the surface of the soil, which means they will be more susceptible to heat and drought damage.
It’s much better to water once per week, but water deeply.
Some years back, a number of municipalities encouraged home-owners to “tuna can their lawns”.
The idea was that a healthy lawn needs about 3-5 cm of water each week. Placing an empty tuna can on your lawn thus provided a helpful gauge of how much to water.
Of course, these days, savvy gardeners know that replacing your lawn with drought-tolerant native plants is an even better water conservation strategy.

## Slide 30: 5b. Tips for containers
Different types of containers have differing water requirements.
Size, location and what the container is made of all matter.
Notes: Containers can be particularly challenging and may require watering more than daily during hot periods.
Container materials such as clay and choir evaporate water through the sides of the container, so they require lots of watering.
Note the mineral salts on the outside of this clay container. This shows how water leaches through the clay, so the container needs to be watered more frequently.
Coir planters, like the one on the right, can look very attractive, but they wick water like crazy.
In the City of Victoria, where they use a lot of coir baskets for street plantings, the municipality adds a layer of foam carpet under-padding inside the baskets. The foam soaks up water and releases it back to the plants as they require it, so the city doesn’t have to water quite so often.
Small containers will generally need to be watered more frequently than larger ones.
Containers in full sun need more water than those growing in shady locations.

## Slide 31: 5b. Tips for containers
Notes: Self-watering containers can make the gardener’s life easier and deliver water where it is most needed – at the roots of the plants.
This is a simply DIY design, requiring only a storage bin and a couple of lengths of PVC tubing
On the right is a “sub-watering” system, similar to many commercially-available self-watering containers.
The idea is there is a water reservoir at the bottom of the container that holds water.
As the soil above dries, water is wicked upwards from the reservoir and becomes available to the roots of plants in the container.

## Slide 32: 5c. Precision watering – Watering spikes
Notes: This raised bed is along the side of our house at the top end of the driveway.
Because it is so close to the house, part of it is actually in a “rain shadow”, under the eaves of the house.
That’s where you can see I’ve added those upside down pop bottles.
What you can’t see is that there is a watering spike attached to the neck of each bottle.
In theory, I can pour water into the open end of the pop bottle and it will slowly infiltrate into the soil.
In practice, I did not find the water spikes worked all that well. Either the little holes got clogged with soil and no water escaped, or the holes worked really well and the water in the bottles drained into the soil immediately.

## Slide 33: 5c. Precision watering – Ollas
Notes: Pronounced “oyas”, this is an old water conservation strategy for hot, dry climates.
The olla is an unglazed pottery container that has been fired at low temperature so it remains quite porous.
The use of Ollas is ancient, and was first documented about 2,000 years ago in China.
This system is used in Pakistan, India, Iran, Mexico and Brazil.
Irrigation with ollas is said to be up to 10 times more efficient than conventional surface watering.
The olla is mostly buried underground.
Then filled through a hole in the top so it releases water slowly into the surrounding soil through pores in the pottery. The image at top right illustrates what this looks like in cross-section.
The water seeps into the soil at a rate that provides adjacent plants with a constant water source at the roots.
In general, the water will travel about twice the diameter of the olla. For example, plants 20 cm from a 10 cm diameter olla should still benefit from its water.
The lid prevents water from evaporating, and stops mosquitos and other bugs using the olla as a repository for their eggs.
Ollas can save around 50 to 75% of the water that traditional watering uses, depending on what plants you have.
Don’t use them around woody rooted plants as those roots can grow around the olla and eventually break it.
In a Canadian context, ollas should be dug up in fall so the winter freeze-thaw cycle doesn’t break them.
Ollas can be purchased or home-made from found materials such as old clay pots. If making your own, check the porosity of the clay pots you are using. Some are fired at higher temperature so they are more durable, but this also makes them less porous and less effective as watering devices.
Another advantage of the olla is that the surface of the soil stays mostly dry, which means that weeds are less likely to sprout.
In the lower photo, we can see the lid of an olla in the middle of those lush looking lettuce plants.

## Slide 34: 5c. Precision watering – Drip irrigation
Notes: Moving up the scale of sophistication – and cost – here we see an example of a drip irrigation system.
This is an interesting example of a drip irrigation system that uses the olla concept.

## Slide 35: 5c. Precision watering – Drip irrigation
Photo courtesy of Helen Gordon, Waterloo Master Gardeners
Notes: This is a more conventional drip irrigation system.
There are lots of “snip and clip” drip irrigation systems on the market that offer a great deal of flexibility.
Combined with a water timer, these can be both effective, efficient and require very little labour after initial installation.
The downsides are mostly to do with cost and some minor engineering skills required to get everything lined up properly.
There may also be limitations if you do multiple crops in the same season, and the irrigation would have to be adjusted to maximize its effectiveness for each new planting.

## Slide 36: Conserving soil moisture
Soil type and organic matter
Mulching
Create shade
Notes: Why are we starting this section with soil type?
The type of soil you have, specifically the texture of your soil, has a huge impact on your garden’s ability to retain water and, therefore, on how much work you need to do to retain water.
If you have sandy soil, like mine, you need to do a lot of work to maintain soil moisture!

## Slide 37: 6a. Soil type and organic matter
Notes: So we need to start by knowing the texture of our soil.
In terms of soil texture, there are three basic types of soil – sand, loam and clay.
If you don’t yet know what kind of soil you have, there are a few very simple tests.
The illustration here is of what’s called the “jar test”.
  Remember to take a soil profile. Try to scoop up soil from the full depth of your trowel, not just a bit scraped off the surface.
  Put your soil into a bit glass jar.
  Add water, shake and then let it sit for a day or two until all sediment has settled.
  Sand particles are larger and heavier, so they will settle to the bottom of the jar.
  Clay particles are the smallest and lightest, so they wind up on top of the pile.
  The relative proportions of each type of material tells you what kind of soil you have.
Another fun soil test to do, especially with kids, is the squeeze test.
  Scoop up a trowel-full of soil. Once again, ensure that you get the full depth of the trowel into the soil so you get a kind of soil profile, not just the soil sitting at the surface.
  Mix this up in a basin of water.
  Then grab a handful of the resulting mud and squeeze until it oozes out between your fingers.
  If the result is long “worms” of soil squeezing out between your fingers, then you have predominantly clay soil.
  If you only get little dollops of soil that drop off almost immediately, then you have mostly sand soil.
So why do we care about soil texture?
  The coarser your soil, the faster water will drain away.
  More sand generally means less water retention. It also means that your soil will naturally contain fewer nutrients than a loam or clay soil.
I garden on what is basically beach sand.
After 30+ years of consistent soil amendments, I can now dig down about 6 cm before the soil is grey.
At a depth of about 10 cm, I hit a fine white sand that is every beach-goers’ dream and every gardeners’ nightmare.
Gardeners with clay soil have the opposite problem. Their soil may contain more nutrients, but it can water-log really easily because drainage is always going to be a challenge.
Plants can be killed as easily by water-logging as from drought.
Water-logged soil can also give rise to anaerobic decomposition, which smells nasty and creates bacteria that are harmful to plants and other soil organisms.
Adding organic material to clay soil will help ensure better drainage and better nutrient uptake by plants.
For those gardeners lucky enough to have a loam soil, you’ve got the best of both worlds.
Your soil will drain at a moderate rate, and contains relatively good nutrient composition.
However, adding organic material can benefit even those with loam soil.
So the moral of this story is that you can’t go wrong by amending your soil.
Furthermore, you cannot fundamentally change the composition of your soil, which means soil amendments are an ongoing job.

## Slide 38: 6b. Mulching
Photo courtesy of Susan Bicket, MGOC.
Notes: Mulch is any material that covers the surface of the soil, reduces weeds, helps prevent moisture evaporation and insulates soil from temperature extremes.
Linda Chalker Scott has a great hour-long video on mulches
She divides them into these categories:
  Living mulches, like ground covers and cover crops. These can be a lot of fun and really add to your garden design. Once established, they are not a lot of work, although you might end up having to restrain some of the more enthusiastic spreaders. Keep in mind that living mulches will also use water in the soil.
  Synthetic mulches includes all those geotextile fabrics, weed blankets, plastic and rubber. I use a red plastic mulch over a drip irrigation system with my tomato plants because it promotes earlier flower and fruit setting. But otherwise, stay away from these. In many cases they are not permeable to water. They do not block weeds and they can really damage your soil. Plus nothing looks uglier than landscape fabric poking out from underneath a pile of mulch.
  Inorganic mulches include rocks, bricks, lava stone, even beach glass. Stone works really well to block predation by squirrels and other critters, especially in a container. It can be a bit of a pain to keep clean. And on really hot days, it can get so hot it actually burns the plants near it.
  Organic mulches include bark, cardboard, newsprint, straw, nut shells, pine needles and wood chips. Organic mulches will break down to help amend your soil, so they need to be replaced periodically.
Note of caution: avoid using cedar mulch on garden beds. It will not break down.
Linda is a big fan of wood chips. Her research shows it to be the best kind of mulch for our northern climate.
Studies have found wood chips to be one of the best performers in terms of moisture retention, temperature moderation, weed control, and sustainability.
Linda’s research has also demonstrated that most of the myths about wood chips are not true.
  Wood chips will not burn easily. They actually absorb water really well, which makes them an ideal mulch in a waterwise garden.
  Wood chips will not acidify your soil. Soil pH comes from the subsoil, not what you put on the surface.
  Wood chips will not deplete your soil of nitrogen. In fact, they will enrich your soil as they break down. There may be a nitrogen deficit at the horizon between the soil and wood chips, but it exists only in a very narrow band. If you are applying wood chips for the first time, you can add a thin under-layer of compost first. This mimics what you will find in the soil profile of a forest floor, but it really isn’t necessary.
  Wood chips also will not transmit diseases to otherwise healthy plants.
As an added bonus, many arborists will give you wood chips for free.
Note, wood chips should be applied to the surface of the soil, but NOT dug in. Digging in wood chips can result in transmission of disease by placing potentially diseased wood chips into close proximity with plants’ roots.

## Slide 39: 6c. Create shade
Notes: On really hot days, temporary shade structures can help retain moisture in the soil and offer protection for delicate plants.
Something as simple as a beach umbrella can help extend the life of lettuce in the garden and slow bolting
The image in the upper right corner is from Nikki Jabbour’s website. She claims to get about 2 extra weeks from her lettuce plants by giving them a bit of shade.
Nikki’s structure depends on hoops to support the shade cloth
The image in the lower right corner is from Sustainable Gardening Australia’s website.
It’s a relatively simple structure to build and stores more easily than do the hoops.

## Slide 40: 7. Plant selection
Does it have to be drought tolerant?
Establishing plants
Characteristics of xeric plants
Notes: By this point in the presentation, you may be wondering if you are going to have to restrict the types of plants you use.
How about a garden of cactus, succulents and yuccas?

## Slide 41: 7a. Does it have to be drought tolerant?
Photo by Carol English
Notes: So the short answer is …
NO – you should not feel that you can only plant drought tolerant or xeric plants
The key is to plant the right plant in the right place and make sure that it is well established.
This is my back yard, taken early afternoon in June 2020.
The shade comes from maples in neighbouring gardens. I have a lot of dry shade. And some very exposed spots that get full sun for much of the day.
Using a lot of native plants, ensuring they get well established, and grouping them according to watering needs allows me to grow a very lush looking garden.

## Slide 42: 7b. Establishing plants
Check the roots first
Dig a big enough hole
Position plant at the right height
Water well immediately on transplant
Re-water until soil is evenly moist.
First 2 weeks – water daily (unless it rains)
First month – water 2-3X weekly
After that, water only when top 2-3 cm of soil are dry – then water deeply.
Notes: Try to transplant at the right time – early evening on a cloudy day is ideal. By late afternoon, plants are already going dormant so transplanting at this time is like operating with anesthetic.
To get a plant established, you need to make sure its roots can get established.
Most gardeners know to check the roots of potted plants to make sure they are not compacted.
If they are, you can gently tease them out.
Some sources also recommend rinsing some or all of the pot soil off the roots.
If the soil in the pot is richer than your garden soil, the plants roots may not want to stray from this nice rich base.
Make sure you dig a big enough hole. It should be 1½ -2 times the size of the root ball.
Plant at the right depth. Different plants will tolerate different depths. For peonies and bearded irises, go shallow. For tomato seedlings, go deep. For most plants, plant at the same depth it was in the pot.

## Slide 43: 7c. Characteristics of xeric plants
Leaves:
Fleshy, succulent – e.g., sedums, cacti
Hairy – e.g., Rudbekia hirta
Silvery – e.g., lamb’s ears (Stachys byzantina)
Leathery – Leatherleaf shrub (Chamaedaphne calyculata)

## Slide 44: 8. Putting it all together
Thinking in terms of hydro zones
Xeriscaping
Beauty shots

## Slide 45: 8a. Thinking in terms of hydro zones
Notes: This is the view from my kitchen window.
The foreground is what I call my “beauty bed” because it houses all the big showy flowers like, peonies, irises and lilies.
These flowers need a fair bit of water, so they are conveniently close to the garden tap, which is out of frame at the bottom of the picture.
Around the beauty bed are two containers that also require a lot of water – a bin of potatoes on the left and a canna lily in the right foreground.
In the middle back left is the bog garden, looking very lush because it is actually inside the pond, so the soil is constantly moist.
You may just be able to see the dark leaves of a colocasia that spends its summers in the bog garden.
Other bog garden plants include a number of natives – chelone, boneset and a few marsh sedges.
At the back of the photo is a hazelnut bush, which adds another layer of shade and makes the bed underneath it very dry.
This dry shade bed is home to a small garden bed of native woodland plants – Canadian ginger, bloodroot and ostrich or fiddlehead ferns.

## Slide 46: 8a. Thinking in terms of hydro zones
Dark blue is the pond
Paler blue beside the pond is a bog garden
Tap is next to the deck
Driest areas are under mature trees and under the eaves of the house
Understanding how much water reaches the soil in each location helps plan better plant selection
Notes: So this is what a rough hydrozone diagram of my back garden looks like.
Although there is lots of shade, the mature maples providing that shade also block some of the rain, and soak up a lot more of it.
And because I like to use every inch of potential garden space, I also have beds underneath the eaves of my house, where there is almost no precipitation.
Consequently, there are some very dry areas around the perimeter of my garden.

## Slide 47: 8b. Xeriscaping
Wikipedia Definition: Xeriscaping is the process of landscaping, or gardening, that reduces or eliminates the need for irrigation.
LCS – Myth of xeric plants – they can actually suck up more moisture than regular plants!
Compromise: group plants according to water needs.
Notes: The term xeriscape was defined and trademarked by the Denver Water Board in 1981. It means that your design incorporates low-water-use plants somewhere in the landscape, and that you group plants together that have similar water requirements (hydrozoning).
Linda Chalker Scott provides a cautionary note to the use of this term. A lot of xeric plants have evolved to store and use water when its available. In this sense, they are a bit like camels. They will soak up whatever water you give them.
As a result, studies have shown that gardeners who, with the best of intentions, plant xeric plants, often end up using MORE water.

## Slide 48: 8c. Beauty shots
Plants growing near a water filtration plant, including a mix of water lovers (e.g., astilbe) and xeric plants, like Russian sage
Photo credit Ellen Eyman, Toronto Master Gardeners

## Slide 49: 8c. Beauty shots
Photo credit Sean James

## Slide 50: 8c. Beauty shots
Notes: Lots of native plants in view here – a relatively simple planting, but attractive and drought-tolerant

## Slide 51: 8c. Beauty shots
Photo credit Gillian Boyd, MGOC
Notes: We’ll end with a local beauty shot from the front garden of Master Gardener Gillian Boyd. Most of the plants you see here are natives.

## Slide 52: Conclusions
Analyse where water runs off your garden.
Rethink garden design and hardscaping to slow or prevent run-off.
Invest in water capture technology
Water wisely – right amount, right frequency, right time of day, right technology
Retain soil moisture via soil amendments, mulch and shade
Place plants according to hydro-zones
Transplant properly and take time to get plants properly established.
Enjoy the results, save money & feel virtuous.

## Slide 53: Q&A
?

## Slide 54: Where to find us – Où nous trouver
Master Gardeners of Ottawa-Carleton
Questions on zone 4a thru 5b only please.
Website: http://mgottawa.ca
Facebook: https://www.facebook.com/groups/819730788084134/
EMAIL: mgoc_helpline@yahoo.ca We try to respond within 48 hours.
Seasonal Market Clinics:
In non-COVID times
Byward, Carp, Cumberland, Main Street, North Gower,
Ottawa, Parkdale, Riverside South, Westboro, Kemptville
Special Events:
Ottawa Home & Garden Show, Seedy Saturday, Carp Garlic Festival, Richmond Fair